### Iteration 3 (continued from progress report)
The polygon-circle collision detection I first implemented would only detect a collision if their edges were overlapping. If one enclosed the other, it would not detect it. (Unlikely to be a problem with bodies of similar sizes.)
I decided to rewrite this to use the same algorithm as polygon-polygon collision detection.
Projecting a circle onto an axis is easier than projecting a polygon – you just project the centre point and then extend it by the radius in each direction.
To reduce duplicate code, I created a Range class, containing a minimum and maximum float value. It contained a method to extend the range to include a value, as well as methods to project a polygon or circle onto an axis.
This made the polygon-polygon and the polygon-circle tests almost identical, as they both involve projecting the bodies onto an axis, and testing whether the projected ranges overlap.
#### Testing
I decided the easiest way to test the collision detection was to be able to click on and drag the bodies around the screen.
Doing this required a test for whether a given point (the mouse pointer) is inside a body. For circles, this is easy, as you can just check the distance to the centre, and compare to the radius.
For polygons, first I checked the point against the bounding box of the polygon. If inside, I then check if the point is inside the polygon by projecting a ray from the point along the x axis and checking it against each edge of the polygon.
If it intersects an even number of edges, the point is outside. If odd, the point is inside the polygon.

One notable bug was discovered at this point in testing. Polygons were colliding slightly before they should have, as if they had an invisible line running from some of
Vector2D side = v1[i+1] – v1[i];
Vector2D axis = Vector2D(axis.y, -axis.x);
The second line incorrectly used axis.y and axis.x when it should have been side.y and side.x. Note that axis was being referenced and initialised on the same line – this error was not caught by the compiler, but meant that the x and y values would contain whatever data was in the memory location previously.
When the second line was corrected, the collision detection code worked correctly.